## Slide 1
PHASE 1 — FOUNDATION
Soldering Bootcamp
Every kid solders something.
Say Watt Robotics · ROV Team | 2026–2027 MATE ROV Season
CLASS 1.2 · ONE SESSION · MADISON, ALABAMA
Notes: Open with energy — this is the week the team has waited for: today everyone solders. 30 seconds here. Set the tone — it is our longest meeting, by design, and the work is worth the time.

## Slide 2
THE MEETING
Three hours, all hands on irons.
0:00
Welcome & Safety Brief
15 min
0:15
Why Soldering Matters
15 min
0:30
Recap & the five moves
25 min
0:55
Hands-on practice joints
60 min
1:55
Break
10 min
2:05
Practice — every kid steady
30 min
2:35
Inspect & certify joints
15 min
2:50
Wrap-up & homework
10 min
We run on time. Every block has a clock, and we hold to it — that habit is part of the engineering.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.2 — SOLDERING BOOTCAMP · 2 / 16
Notes: Walk the eight blocks quickly, then land one point: this is our longest day, about three and a half hours. If a block runs long, we protect the hands-on practice and trim elsewhere — we never cut the time on the iron. Note the break at 1:55.

## Slide 3
01
SECTION 01
Welcome &
Safety Brief
0:00 – 0:15 · 15 MIN
Every meeting we ever hold will begin in exactly this place.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.2 — SOLDERING BOOTCAMP · 3 / 16
Notes: Same opening as always. Let the CEO run the safety brief if roles are set — 60 to 90 seconds. The ritual matters more today than ever: there are hot irons in the room.

## Slide 4
THE STANDING RITUAL
Every meeting opens with a safety brief.
Why we do this
Real engineering and dive teams brief safety before every job — not because something went wrong, but so it never does. We adopt the same habit on day one. Sixty seconds, every meeting, no exceptions.
Each brief answers the same four questions, so the team always knows what to expect.
1
What are we doing today?
2
What could hurt someone?
3
How do we prevent it?
4
Who do we tell if something happens?
TODAY'S BRIEF · CLASS 1.2
THE WORK
First solder joints, the kit unboxing, and the first real electronics on the robot.
THE HAZARDS
Soldering irons at roughly 700°F. Burns, lead and flux fumes, and hot solder spatter.
PREVENTION
Irons in their stands, never on the bench. Fume fan on. Safety glasses down, hair tied back. Wash hands after handling solder.
IF SOMETHING HAPPENS
Cool a burn under running water, tell the advisor, and log it. Every burn gets reported — even a small one.
LOOKING AHEAD
Class 1.3 — the kit comes out of the box and takes its first electronics.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.2 — SOLDERING BOOTCAMP · 4 / 16
Notes: The most important safety brief of the season so far. Slow down on hazards and prevention. Irons live in their stands, never on the bench. Confirm the fume fan is on and everyone has glasses before any iron is powered. Read ‘every burn gets reported’ out loud.

## Slide 5
02
SECTION 02
Why We
Solder
0:15 – 0:30 · 15 MIN
Before anyone touches the kit, everyone understands why a good joint matters.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.2 — SOLDERING BOOTCAMP · 5 / 16
Notes: Short divider, 15 minutes. Set up the why before the how: nobody picks up an iron until they understand what a good joint is and why it matters.

## Slide 6
WHY WE SOLDER
A robot is only as good as its weakest joint.
Soldering fuses two wires into one connection that holds — electrically and mechanically. Every thruster, sensor, and camera on our ROV reaches the control box through a joint someone made by hand.
A good joint is shiny, solid, and stronger than the wire around it. A bad one — cold, dull, or barely touching — works on the bench, then fails in the water, mid-mission, where we cannot reach it.
This is the first real engineering skill of the season. Today, every kid earns it.
THE STANDARD
Shiny, solid, and built to last the season.
A joint you would trust at 2.5 m
In the dark, with the mission clock running, where nobody can fix it.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.2 — SOLDERING BOOTCAMP · 6 / 16
Notes: Make it concrete — the robot fails at its weakest joint, and that joint is one a kid will make today. Two minutes. Land the bold line: this is the first real engineering skill of the season, and every kid earns it today.

## Slide 7
KNOW YOUR JOINT
Three joints. Know them on sight.
COLD JOINT
Dull and
grainy
Too little heat. The solder sits on top in a dull blob instead of flowing in. Looks done, fails later. Reflow it.
GOOD JOINT
Shiny and
smooth
Heat on the joint, solder wicks around the wire in a bright cone. Strong and clean. This is the target.
BRIDGED JOINT
Touching
its neighbor
Too much solder jumps to the next pad and shorts them together. Wick the extra away and redo it.
Every kid makes all three today — and learns to tell them apart by eye.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.2 — SOLDERING BOOTCAMP · 7 / 16
Notes: Hold up real examples if you have them. Walk the three: cold (dull blob), good (shiny cone), bridged (shorted). Tell them they will make all three today — making the bad ones on purpose is how they learn to see the good one.

## Slide 8
03
SECTION 03
Soldering
Bootcamp
0:30 – 1:55 · 85 MIN
Watch it done, see it done, then do it — every kid, hands on an iron.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.2 — SOLDERING BOOTCAMP · 8 / 16
Notes: This is the heart of the day, 85 minutes. Set the flow: watch, then demo, then everyone practices. Energy up — the clock is generous here on purpose.

## Slide 9
BEFORE CLASS
Watch it at home. Build it in class.
The concepts come from MATE’s own instructors. Watch these short presentations before class, so every minute of our meeting is spent at the bench, not at a screen.
As you watch, notice: how to tin the tip; why the heat goes on the joint, not the solder; what a good joint looks like; and how heat-shrink and strain relief protect the wire.
Come ready to solder — in class we recap, demo once, and then it’s hands on irons.
PRE-WATCH HOMEWORK
Three short videos, then straight to the iron.
MATE: Soldering & Waterproofing Wires
Plus MATE: Using Tools (20–30 min) and How to Solder (22 min) — all assigned on the team site.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.2 — SOLDERING BOOTCAMP · 9 / 16
Notes: Cue the 22-minute video before the meeting so it is ready to play. Read the four ‘watch for’ prompts aloud first so they watch actively. Pause on the key moments — tinning the tip, heat on the joint. Then go straight to the bench while energy is high.

## Slide 10
THE DEMONSTRATION
The moves, start to finish.
1
Strip
BARE THE WIRE
Strip about 5 mm of insulation. Clean, bright copper — no nicks in the strands.
2
Tin the tip
PREP THE IRON
Wet sponge, then a fresh dab of solder on the tip. Do this before every single joint.
3
Heat the joint
IRON ON METAL
Press the iron to the wires, not the solder. Count two seconds to let them heat.
4
Feed the solder
LET IT FLOW
Touch solder to the hot joint, not the iron. It melts and wicks in. Then stop.
5
Heat-shrink
SEAL THE JOINT
Slide shrink tube over the joint and heat it. Add a service loop for strain relief.
6
Inspect
CHECK YOUR WORK
Hold it to the light. Shiny and solid? Done. Dull or lumpy? Reflow and try again.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.2 — SOLDERING BOOTCAMP · 10 / 16
Notes: Demonstrate each move once as you walk these six cards — this is the teach-once moment, about 15 minutes. Section 4.3: you show it, then you step back. Do not solder for them after this.

## Slide 11
HANDS ON
Now everyone makes one.
1
Strip and tin a wire
Each kid strips a wire and tins it. We check for clean copper and a shiny tip before moving on.
2
Make your first joint
Join two tinned wires. Heat the joint, feed the solder, then let it cool without moving it.
3
Heat-shrink and strain relief
Slide the tube, shrink it, and add a service loop so the wire never pulls on the joint itself.
4
Inspect and redo
Hold it to the light. Shiny and solid moves on; dull or lumpy gets reflowed. Redoing it is the lesson.
Two things to remember. No one opens the kit until they have made one joint they are proud of. The redo is not failure — it is the skill arriving.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.2 — SOLDERING BOOTCAMP · 11 / 16
Notes: This block cannot be cut. Every kid makes a joint, inspects it, and redoes it if needed. Circulate, photograph, encourage — hands off the irons. Expect it to run long; that is fine. Nobody opens the kit until they have made a joint they are proud of.

## Slide 12
HOW WE LEARN
Teach once. Then step back.
“We show a skill one time — then we step back and let them struggle to it. The struggle is where the engineer is made.”
MATE’s Section 4.3 is strict: the work has to be the students’. Adults teach, demonstrate, and keep the room safe — but adults do not build the robot, write the documentation, or hold the iron through the joint.
Parents demonstrate
Show the move once, then photograph and encourage. Hands stay off the work — even when it is slow.
Students do the work
Every joint, every fix, every redo is theirs. Slow and real beats fast and borrowed.
Help is disclosed
Any outside help — including AI — gets written into the documentation. Honesty is scored in April.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.2 — SOLDERING BOOTCAMP · 12 / 16
Notes: Read the quote slowly — this is the philosophy of the whole season. Make sure every parent hears it: demonstrate, then step back. The struggle is the point. Mention AI disclosure plainly — honesty is scored in April.

## Slide 13
BREAK
Ten minutes.
We resume at 1:55 — hands washed, irons cooling, and we start on time.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.2 — SOLDERING BOOTCAMP · 13 / 16
Notes: Ten minutes. Irons stay on their stands and cool. Hands washed before snacks — solder has lead. Resume at 1:55, on time.

## Slide 14
04
SECTION 04
Wrap-Up &
Homework
2:50 – 3:00 · 10 MIN
Close the loop: what each student carries out, and what the team carries forward into the water.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.2 — SOLDERING BOOTCAMP · 14 / 16
Notes: Final divider — 10 minutes to close the loop. Make sure every kid leaves knowing their homework and the team knows the parallel-track items.

## Slide 15
WRAP-UP & HOMEWORK
Before we meet again.
EVERY STUDENT
1
Practice one clean joint at home — shiny, solid, strain-relieved.
2
Be able to spot a cold joint vs. a good one on sight.
3
Closed-toe shoes again next time — the kit comes out.
THE PARALLEL TRACK · LEADS & ADVISORS
Battery, charger, and leads in hand before the electronics class. SeaMATE lab kits stocked. Pool prerequisites in motion — lifeguard, swim checks, host rules in writing.
NEXT LESSON · CLASS 1.3
Kit Unboxing
& Electronics
The Triggerfish comes out of the box, gets inventoried, and takes its first real connections — plus the team's records and capsule designs open.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.2 — SOLDERING BOOTCAMP · 15 / 16
Notes: Three things for students, no more — keep it light. Read the parallel-track card to the parents: battery before Week 3, pool prerequisites, and the DISL call. These gate the water. Preview Week 3 — electronics finished and the first splash.

## Slide 16
SIX KIDS, SIX IRONS
Now it’s real.
Everyone soldered. The kit is open, the first joints are on the robot, and the capsule is on paper.
Next time, the kit comes out.
SAY WATT ROBOTICS · ROV TEAM | NEXT LESSON — CLASS 1.3, KIT UNBOXING & FIRST ELECTRONICS
Notes: Close with pride — everyone soldered today, the kit is open, the first joints are on the robot. Land the final line: next week, it gets wet. Send them out energized for the first splash.