## Slide 1
PHASE 1 — FOUNDATION
Electronics Workshop
Learn to read a circuit — the meter, switches, and symbols.
Say Watt Robotics · ROV Team | 2026–2027 MATE ROV Season
CLASS 1.4 · ONE SESSION · MADISON, ALABAMA
Notes: Open with energy — this is the week the team has waited for: today everyone solders. 30 seconds here. Set the tone — it is our longest meeting, by design, and the work is worth the time.

## Slide 2
THE MEETING
Three hours, learning to read a circuit.
0:00
Welcome & Safety Brief
15 min
0:15
The Multimeter
35 min
0:50
How Switches Work
20 min
1:10
Simple Circuits Lab
30 min
1:40
Break
10 min
1:50
Build & Measure a Circuit
40 min
2:30
The Electrical Symbols Sheet
20 min
2:50
Wrap-up & homework
10 min
We run on time. Every block has a clock, and we hold to it — that habit is part of the engineering.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.4 — ELECTRONICS WORKSHOP · 2 / 16
Notes: Walk the eight blocks quickly, then land one point: this is our longest day, about three and a half hours. If a block runs long, we protect the hands-on practice and trim elsewhere — we never cut the time on the iron. Note the break at 1:55.

## Slide 3
01
SECTION 01
Welcome &
Safety Brief
0:00 – 0:15 · 15 MIN
Every meeting we ever hold will begin in exactly this place.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.4 — ELECTRONICS WORKSHOP · 3 / 16
Notes: Same opening as always. Let the CEO run the safety brief if roles are set — 60 to 90 seconds. The ritual matters more today than ever: there are hot irons in the room.

## Slide 4
THE STANDING RITUAL
Every meeting opens with a safety brief.
Why we do this
Real engineering and dive teams brief safety before every job — not because something went wrong, but so it never does. We adopt the same habit on day one. Sixty seconds, every meeting, no exceptions.
Each brief answers the same four questions, so the team always knows what to expect.
1
What are we doing today?
2
What could hurt someone?
3
How do we prevent it?
4
Who do we tell if something happens?
TODAY'S BRIEF · CLASS 1.4
THE WORK
Multimeters and simple circuits — measuring and reading, not yet wiring the robot.
THE HAZARDS
Low-voltage circuits and batteries; the soldering iron if we tin a lead.
PREVENTION
Set the meter before connecting; never short a battery's terminals; irons in stands if used.
IF SOMETHING HAPPENS
Stop, disconnect the battery, tell the advisor, and log it.
LOOKING AHEAD
Class 1.5 — the control box build begins (the long one).
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.4 — ELECTRONICS WORKSHOP · 4 / 16
Notes: The most important safety brief of the season so far. Slow down on hazards and prevention. Irons live in their stands, never on the bench. Confirm the fume fan is on and everyone has glasses before any iron is powered. Read ‘every burn gets reported’ out loud.

## Slide 5
02
SECTION 02
The
Multimeter
0:15 – 0:50 · 35 MIN
Before we trust a wire, we learn to read it.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.4 — ELECTRONICS WORKSHOP · 5 / 16
Notes: Short divider, 15 minutes. Set up the why before the how: nobody picks up an iron until they understand what a good joint is and why it matters.

## Slide 6
THE MULTIMETER
Your window into the circuit.
A multimeter measures what your eyes can't: voltage (the push), continuity (is the path complete?), and current (the flow). With it, a kid can prove a wire is good before trusting it on the robot.
It is also how you find a fault. A dead thruster is usually an open circuit somewhere — a broken joint or a loose screw. The meter walks the path and finds the gap.
Measure, don't guess. The meter turns 'I think it's wired right' into 'I know it is.'
OHM'S LAW
Voltage = Current × Resistance.
V = I × R
The one equation behind every reading. From the reading: Underwater Robotics, Ch 8 §4.4.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.4 — ELECTRONICS WORKSHOP · 6 / 16
Notes: Make it concrete — the robot fails at its weakest joint, and that joint is one a kid will make today. Two minutes. Land the bold line: this is the first real engineering skill of the season, and every kid earns it today.

## Slide 7
WHAT IT MEASURES
Three readings. Know what each tells you.
VOLTAGE
The
push
How hard the electricity is being pushed, across two points. Our system runs at 12 volts.
CONTINUITY
A closed
loop
Is the path complete? A beep means the circuit is closed. No beep means an open — a break to find.
CURRENT
The
flow
How much is flowing, in amps. Too much means a short or overload — the reason we fuse the circuit.
Voltage, continuity, current — the three questions the meter answers.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.4 — ELECTRONICS WORKSHOP · 7 / 16
Notes: Hold up real examples if you have them. Walk the three: cold (dull blob), good (shiny cone), bridged (shorted). Tell them they will make all three today — making the bad ones on purpose is how they learn to see the good one.

## Slide 8
03
SECTION 03
Switches &
Circuits
0:50 – 1:40 · 50 MIN
A switch, a battery, a light — the whole idea of a circuit in your hands.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.4 — ELECTRONICS WORKSHOP · 8 / 16
Notes: This is the heart of the day, 85 minutes. Set the flow: watch, then demo, then everyone practices. Energy up — the clock is generous here on purpose.

## Slide 9
BEFORE CLASS
Watch it at home. Build it in class.
MATE's instructors teach the electronics on video. Watch these before class so our meeting time goes to measuring, wiring, and building — not slides.
As you watch, notice: how to set the meter's dial, how a switch makes and breaks a circuit, and how a simple circuit carries current from battery to load and back.
Come ready to measure and build — we pick up the meter at the door.
PRE-WATCH HOMEWORK
Three short videos, then straight to the bench.
MATE: Multimeter Basics
Plus MATE: How Switches Work and Simple Circuits — all assigned on the team site.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.4 — ELECTRONICS WORKSHOP · 9 / 16
Notes: Cue the 22-minute video before the meeting so it is ready to play. Read the four ‘watch for’ prompts aloud first so they watch actively. Pause on the key moments — tinning the tip, heat on the joint. Then go straight to the bench while energy is high.

## Slide 10
THE LANGUAGE OF CIRCUITS
Six symbols you'll see all season.
1
Wire
A CONDUCTOR
A straight line carries current. A dot where wires connect; a hop where they cross without touching.
2
Battery
THE SOURCE
Long line positive, short line negative. The push that drives the circuit.
3
Switch
THE GATE
Opens and closes the path. SPST, SPDT, DPDT — the kinds you'll wire in the control box.
4
Resistor
LIMITS FLOW
A zigzag. Slows the current so a component gets just what it needs.
5
LED
A LIGHT
A diode that lights up — and only works one way around. Polarity matters.
6
Fuse
THE SAFETY
Breaks the circuit if current gets too high. Sized to the full-load amps.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.4 — ELECTRONICS WORKSHOP · 10 / 16
Notes: Demonstrate each move once as you walk these six cards — this is the teach-once moment, about 15 minutes. Section 4.3: you show it, then you step back. Do not solder for them after this.

## Slide 11
HANDS ON
Build a circuit that works.
1
Read the schematic
Start from the symbols: battery, switch, resistor, LED. Know the path before you wire it.
2
Build it on the board
Wire the Simple Circuits Lab Kit to match the schematic. One group, one circuit.
3
Flip the switch
Close the circuit and the LED lights. Nothing? You have an open — walk it with the meter.
4
Measure and prove it
Read the voltage across the LED and the continuity of each leg. Confirm it matches the plan.
Two things to remember. Every kid builds and measures one working circuit before we touch the control box.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.4 — ELECTRONICS WORKSHOP · 11 / 16
Notes: This block cannot be cut. Every kid makes a joint, inspects it, and redoes it if needed. Circulate, photograph, encourage — hands off the irons. Expect it to run long; that is fine. Nobody opens the kit until they have made a joint they are proud of.

## Slide 12
A COMPETITION DIVIDEND
Keep the symbols sheet. Forever.
The Electrical Symbols handout uses the same standard your competition SID will be graded against. The sheet you learn on today is the sheet you draw from in April.
MATE's Electrical Symbols handout is free and small, but it is one of the highest-leverage pages of the season. Print it, three-hole punch it, and keep it in the notebook all year.
The handout
MATE's one-page key to every schematic symbol. Free to print.
The SID
Your System Integration Diagram — a required, scored competition document drawn in these exact symbols.
Keep it forever
The standard doesn't change. Today's reference becomes April's grading rubric.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.4 — ELECTRONICS WORKSHOP · 12 / 16
Notes: Read the quote slowly — this is the philosophy of the whole season. Make sure every parent hears it: demonstrate, then step back. The struggle is the point. Mention AI disclosure plainly — honesty is scored in April.

## Slide 13
BREAK
Ten minutes.
We resume in ten — meters down, hands clear of the bench.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.4 — ELECTRONICS WORKSHOP · 13 / 16
Notes: Ten minutes. Irons stay on their stands and cool. Hands washed before snacks — solder has lead. Resume at 1:55, on time.

## Slide 14
04
SECTION 04
Wrap-Up &
Homework
2:50 – 3:00 · 10 MIN
Name what happens next — and stage the parts before the holiday break.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.4 — ELECTRONICS WORKSHOP · 14 / 16
Notes: Final divider — 10 minutes to close the loop. Make sure every kid leaves knowing their homework and the team knows the parallel-track items.

## Slide 15
WRAP-UP & HOMEWORK
Before we meet again.
EVERY STUDENT
1
Practice reading a simple schematic — battery, switch, resistor, LED.
2
Keep your Electrical Symbols handout in your notebook — you'll use it all year.
3
Software Lead: make sure the repo is ready for wiring notes.
THE PARALLEL TRACK · LEADS & ADVISORS
The control box is a long build (MATE budgets six hours) — stage the kit's control-box parts and the soldering stations. Battery in hand.
NEXT LESSON · CLASS 1.5
Control Box
Part I
We build the PufferFish practice board, then start the TriggerFish REV 4 control box — the topside brain that drives the thrusters.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.4 — ELECTRONICS WORKSHOP · 15 / 16
Notes: Three things for students, no more — keep it light. Read the parallel-track card to the parents: battery before Week 3, pool prerequisites, and the DISL call. These gate the water. Preview Week 3 — electronics finished and the first splash.

## Slide 16
READ THE CIRCUIT
Now they can read it.
Every kid can measure a circuit, read the symbols, and build a working one. The language of electronics is theirs.
Next, the control box.
SAY WATT ROBOTICS · ROV TEAM | NEXT LESSON — CLASS 1.5, CONTROL BOX I
Notes: Close with pride — everyone soldered today, the kit is open, the first joints are on the robot. Land the final line: next week, it gets wet. Send them out energized for the first splash.