## Slide 1
PHASE 1 — FOUNDATION
Week 5 — Control Box I
PufferFish first. Then we touch the real board.
Say Watt Robotics · ROV Team | 2026–2027 MATE ROV Season
MEETING 5 · THREE HOURS · MADISON, ALABAMA
Notes: Open with the frame: tonight is the bridge between practice and the real thing. The kids should hear 'we earned this' explicitly. Run the title slide for ~30 seconds, then move.

## Slide 2
AGENDA
Three hours. Practice board, then the real board.
0:00
Welcome & Safety Brief
15 min
0:15
The PufferFish — Practice Board Brief
15 min
0:30
PufferFish — Hands On
45 min
1:15
The TriggerFish REV 4 — Where We Pick Up
15 min
1:30
Break
10 min
1:40
TriggerFish — Next Block of Components
50 min
2:30
Meter-Check Discipline
15 min
2:45
Wrap-Up & Homework
15 min
We run on time. Every block has a clock, and we hold to it — that habit is part of the engineering.
SAY WATT ROBOTICS · ROV TEAM
WEEK 5 — CONTROL BOX I · 2 / 21
Notes: Read the agenda end-to-end. Call out that the break sits between the where-we-pick-up brief and the hands-on block on purpose — kids should be fresh before they touch the real board. ~60 seconds.

## Slide 3
TODAY'S ROLES
Four jobs. Four students. Different every week.
Every meeting we assign these four — by season's end, every student has done every job.
NOTETAKER / SCRIBE
TODAY: __________________________________
Captures every decision, action item, and blocker. Files notes with the CFO for the engineering notebook.
SAFETY BRIEFER
TODAY: __________________________________
Delivers the standing four-question safety brief at the start of the meeting.
PHOTOGRAPHER
TODAY: __________________________________
Captures photos and short videos throughout — feeds the engineering notebook and the marketing display.
TIMEKEEPER
TODAY: __________________________________
Holds the meeting to the agenda's clock. Calls the time at each block change.
SAY WATT ROBOTICS · ROV TEAM
WEEK 5 — CONTROL BOX I · 3 / 21
Notes: Assign the four roles RIGHT NOW. Names on the slide. The Notetaker carries the action-items slide later — they need to know they're on the clock. ~90 seconds.

## Slide 4
SECTION 01
Welcome &
Safety Brief
0:00 – 0:15 · 15 MIN
Same ritual every meeting. We get sharper at it; the kids start running it.
01
SAY WATT ROBOTICS · ROV TEAM
WEEK 5 — CONTROL BOX I · 4 / 21
Notes: Standing ritual. Hand off to the kids if they're ready; you read it once if not.

## Slide 5
THE STANDING RITUAL
Every meeting opens with a safety brief.
Why we do this
Real engineering and dive teams brief safety before every job — not because they expect to fail, but because the discipline of asking the same four questions every time is what makes a team safe in the long run. We start the habit now, when the stakes are small, so it's automatic when they aren't.
1
What are we doing today?
2
What could hurt someone?
3
How do we prevent it?
4
Who do we tell if something happens?
TODAY'S BRIEF · MEETING 5
THE WORK
Soldering through-hole components onto two boards: the SeaMATE PufferFish practice board and the TriggerFish REV 4 control box.
THE HAZARDS
Iron tip at 650°F. Back of the board and component leads are hot too. Metal clippings fly when cutting leads. Lead-based solder.
PREVENTION
Iron in holder when not in use. Fume extractor on, fan blowing away from the student. Safety glasses for snipping. Wash hands when done.
IF SOMETHING HAPPENS
Stop. Speak up. Tell the advisor immediately. Burns get cool water for 15 minutes. Loose iron on the bench? Call it out.
LOOKING AHEAD
1.6 is wiring and power — fewer joints, bigger consequences if a polarity check gets skipped. Habits we set today carry forward.
SAY WATT ROBOTICS · ROV TEAM
WEEK 5 — CONTROL BOX I · 5 / 21
Notes: Either you deliver this or the assigned Safety Briefer does — choose at the top of the meeting. Move through the four standing questions, then the today's-brief card. Slow down on PREVENTION; the back-of-board heat hazard is the one new solderers forget.

## Slide 6
SECTION 02
Practice
First
0:15 – 1:15 · 60 MIN
The PufferFish board is a low-stakes circuit. We earn the technique here before we touch the real one.
02
SAY WATT ROBOTICS · ROV TEAM
WEEK 5 — CONTROL BOX I · 6 / 21
Notes: Section 02 — the PufferFish. Hold the practice-board metaphor: low stakes is the point.

## Slide 7
PUFFERFISH
Earn a clean joint first.
The SeaMATE PufferFish board has nothing to do with the ROV. That's why we use it.
The PufferFish is a small practice circuit MATE built for one purpose: give every kid a low-stakes board to develop the technique on before they sit down at the TriggerFish.
If you mess up a PufferFish joint, you re-flow it, re-do it, or pull the component and try again. If you mess up a TriggerFish joint — a $290 component on a board you only get one of — it's a different conversation.
The frame for the night: working vs. crafted. A working joint passes a multimeter check. A crafted joint also survives heat, vibration, and the trip to the pool. The PufferFish is where we calibrate what crafted feels like.
SAY WATT ROBOTICS · ROV TEAM
WEEK 5 — CONTROL BOX I · 7 / 21
Notes: Walk through this; spend the most time on the headline's verb.

## Slide 8
PUFFERFISH — THE FIVE MOVES
Every joint is the same five moves.
1
Seat the component flush
Bend leads, push through, flip the board, make sure the body is flat against the PCB. A component sitting half a millimeter off is a future failure.
2
Heat the joint, not the solder
Iron tip on the pad AND the lead at the same time, for one full second. The pad has to be hot enough to flow solder on its own.
3
Feed solder into the joint
Touch the solder to the joint — not the iron tip. If it doesn't flow, the joint isn't hot enough yet.
4
Pull the solder, then the iron
Solder first, iron second. The order matters — pulling the iron first leaves a peak; pulling solder first leaves a clean dome.
5
Inspect
Shiny, smooth, concave. Dull or grainy means a cold joint. Re-flow it now, not later.
SAY WATT ROBOTICS · ROV TEAM
WEEK 5 — CONTROL BOX I · 8 / 21
Notes: Walk through this; spend the most time on the headline's verb.

## Slide 9
SECTION 03
TriggerFish
Where We Pick Up
1:15 – 1:30 · 15 MIN
1.3 left us with the fuse holder, the two 1000µF caps, and the 3 A fuse mounted. Here's the next block.
03
SAY WATT ROBOTICS · ROV TEAM
WEEK 5 — CONTROL BOX I · 9 / 21
Notes: Section 03 — picking up the TriggerFish where 1.3 left off. iPad with the Guide should already be queued.

## Slide 10
TRIGGERFISH REV 4
Where we left off — and what comes next.
From 1.3 the board already carries: the fuse holder, two 1000µF / 16V electrolytic capacitors (with polarity verified before commit), the 3 A fuse seated in the holder, and the power leads run through heatshrink.
Tonight we open the SeaMATE TriggerFish ROV Guide on the iPad and pick up at the next block of components per the slide sequence. The Guide is the team's reference of record — every step gets verified against the slide before any iron touches the board.
Polarity rule still applies: every electrolytic cap, every diode, every transistor — verify the orientation against the board silkscreen AND the Guide image before you commit the joint. A reversed electrolytic cap fails open, fails loud, and ends the night.
SAY WATT ROBOTICS · ROV TEAM
WEEK 5 — CONTROL BOX I · 10 / 21
Notes: Walk through this; spend the most time on the headline's verb.

## Slide 11
READING THE GUIDE
Two things on every slide.
THE INSTRUCTION
What the slide says to do. Read it out loud as a team before anyone picks up an iron. If the verb is 'solder,' name what gets soldered and in what order.
THE WARNING
What the slide flags. Polarity. Orientation. Sequence. Any line that says 'double check' or 'verify' gets a second pair of eyes before any commit.
SAY WATT ROBOTICS · ROV TEAM
WEEK 5 — CONTROL BOX I · 11 / 21
Notes: Walk through this; spend the most time on the headline's verb.

## Slide 12
BREAK
Ten minutes.
We resume in ten — and, like always, we start on time.
SAY WATT ROBOTICS · ROV TEAM | WEEK 5 — CONTROL BOX I

## Slide 13
SECTION 04
The Next
Block
1:40 – 2:30 · 50 MIN
Fifty minutes, hands on. Coach John runs the brief; the kids run the build.
04
SAY WATT ROBOTICS · ROV TEAM
WEEK 5 — CONTROL BOX I · 13 / 21
Notes: Section 04 — the next block of components. This is the longest hands-on stretch; let the kids own it.

## Slide 14
THE BUILD LOOP
How we work through the Guide.
1
Read the slide as a team
One person reads it out; the others listen. No iron picked up until the team agrees on what the slide is asking for.
2
Stage the components
Lay them out next to the board, oriented the way they'll go in. Polarity-sensitive parts marked clearly.
3
Solder, one student at a time
Whoever has the iron, owns that joint. Others coach, photograph, or cue up the next component.
4
Inspect and meter-check
Shiny, smooth, concave joint. Continuity to the next pad in the circuit; no shorts to ground or neighboring pads. If the meter doesn't agree, re-flow.
5
Move to the next slide
Only when the current step passes inspection AND meter-check. We don't get ahead of the Guide.
SAY WATT ROBOTICS · ROV TEAM
WEEK 5 — CONTROL BOX I · 14 / 21
Notes: Walk through this; spend the most time on the headline's verb.

## Slide 15
SECTION 05
Meter-Check
Discipline
2:30 – 2:45 · 15 MIN
Three reads, every stage. Continuity good, no shorts, polarity confirmed.
05
SAY WATT ROBOTICS · ROV TEAM
WEEK 5 — CONTROL BOX I · 15 / 21
Notes: Section 05 — meter-check discipline. Don't let this slide get skipped. Three reads, every stage.

## Slide 16
THREE READS
Every completed stage gets metered before we move on.
The watt meter from 1.3 stays on the bench. The multimeter is the workhorse for these reads.
1
Continuity from each new joint to its intended next pad
Beep means the joint connects where the schematic says it does. Silence means re-flow or re-route.
2
No shorts to ground or to neighboring pads
Probe each new pad against ground and against the pads immediately adjacent. Beep here means a solder bridge — fix it before power.
3
Polarity confirmed against the Guide image
Eyes on the silkscreen, eyes on the Guide, eyes on the component. Three references; one orientation. If two agree and one doesn't, stop and figure out which is wrong.
SAY WATT ROBOTICS · ROV TEAM
WEEK 5 — CONTROL BOX I · 16 / 21
Notes: Walk through this; spend the most time on the headline's verb.

## Slide 17
SECTION 06
Wrap-Up &
Homework
2:45 – 3:00 · 15 MIN
Capture what we decided. Close the loop. Hand off the next move.
06
SAY WATT ROBOTICS · ROV TEAM
WEEK 5 — CONTROL BOX I · 17 / 21
Notes: Section 06 — wrap-up. Capture what we decided; close the loop.

## Slide 18
WRAP-UP & HOMEWORK
Before we meet again.
EVERY STUDENT
1
Re-read the SeaMATE TriggerFish ROV Guide slides we covered tonight. If you led a joint, be able to explain why the polarity went the way it did.
2
Bring closed-toe shoes again next week — we power the board up for the first time in 1.6.
3
If you didn't get a turn at the iron tonight, message the CEO so you're at the top of the rotation in 1.6.
THE PARALLEL TRACK · LEADS & ADVISORS
Advisors: confirm the 12V SLA battery, charger, and power leads are in hand by Wednesday — they're the gating items for 1.6's smoke test. Confirm the pre-terminated tether arrived; if not, escalate the order.
NEXT MEETING · WEEK 6
Control Box II
Finish the wiring. Build the ROV's power wire. Connect the tether. Fuse the circuit to measured full-load amps. Meter-check every stage before first power-up.
SAY WATT ROBOTICS · ROV TEAM
WEEK 5 — CONTROL BOX I · 18 / 21
Notes: Read the three student items out loud. Confirm each item has an owner. Hand off to the Notetaker for the action-items slide; they read what they captured and you confirm it.

## Slide 19
ACTION ITEMS
What we decided. Who owns it. When it's due.
The Notetaker fills these in during the meeting and reads them back before we leave.
ITEM
OWNER
DUE
SAY WATT ROBOTICS · ROV TEAM
WEEK 5 — CONTROL BOX I · 19 / 21
Notes: Notetaker fills these in live as decisions are made. Read back before the closer.

## Slide 20
BEFORE WE LEAVE
Tools accounted for. Shop reset.
We do this together, every meeting. No exceptions — the Tool Steward leads.
Soldering irons unplugged, cool, and put away.
PufferFish boards collected; loose components back in the kit.
TriggerFish board secured in its tray; iPad with the Guide returned.
Multimeter and watt meter back in their cases.
Workshop swept; benches wiped.
Today's photos uploaded to the team folder.
Notetaker's meeting notes filed with the CFO for the engineering notebook.
SAY WATT ROBOTICS · ROV TEAM
WEEK 5 — CONTROL BOX I · 20 / 21
Notes: Tool Steward leads. Every kid stays until the workshop is reset.

## Slide 21
PRACTICE EARNED. REAL WORK STARTED.
Next week, we power it up.
The PufferFish taught us the technique. The TriggerFish is where we use it. 1.6 closes the loop with the first smoke test.
SAY WATT ROBOTICS · ROV TEAM | NEXT MEETING — WEEK 6, CONTROL BOX II
Notes: Dark slide. Read the statement, pause, read the italic summary. Don't add commentary — the kids should leave on the line, not on your gloss. ~30 seconds.