## Slide 1
PHASE 1 — FOUNDATION
Week 6 — Control Box II
Finish the wiring. Build the power. Meter-check before the smoke.
Say Watt Robotics · ROV Team | 2026–2027 MATE ROV Season
MEETING 6 · THREE HOURS · MADISON, ALABAMA
Notes: Open with the high-stakes shift. 1.5 was practice on a real board. 1.6 closes the box and stages the smoke test. The discipline tonight is what protects 1.7's pool day. ~30 seconds.

## Slide 2
AGENDA
Three hours. Finish the box, build the power, ready to smoke-test.
0:00
Welcome & Safety Brief
15 min
0:15
Where the Board Stands
15 min
0:30
Finish the Control-Box Wiring
60 min
1:30
Break
10 min
1:40
ROV Power Wire + Tether Connection
45 min
2:25
Fuse Selection from Measured Full-Load Amps
15 min
2:40
Pre-Power-Up Meter-Check (Three Reads × Every Pad)
20 min
3:00
Wrap-Up & Homework
0 min
We do NOT power the board up today. Smoke test waits for 1.7's pre-pool review.
SAY WATT ROBOTICS · ROV TEAM
WEEK 6 — CONTROL BOX II · 2 / 22
Notes: Read the agenda end-to-end. Call out the closing line — we do NOT power up today. Smoke test is at 1.7's pre-pool review. ~60 seconds.

## Slide 3
TODAY'S ROLES
Four jobs. Four students. Different every week.
Every meeting we assign these four — by season's end, every student has done every job.
NOTETAKER / SCRIBE
TODAY: __________________________________
Captures every decision, action item, and blocker. Files notes with the CFO for the engineering notebook.
SAFETY BRIEFER
TODAY: __________________________________
Delivers the standing four-question safety brief at the start of the meeting.
PHOTOGRAPHER
TODAY: __________________________________
Captures photos and short videos throughout — feeds the engineering notebook and the marketing display.
TIMEKEEPER
TODAY: __________________________________
Holds the meeting to the agenda's clock. Calls the time at each block change.
SAY WATT ROBOTICS · ROV TEAM
WEEK 6 — CONTROL BOX II · 3 / 22
Notes: Assign the four roles. The Photographer matters tonight — the pre-power-up meter-check is photo gold for the engineering notebook. ~90 seconds.

## Slide 4
SECTION 01
Welcome &
Safety Brief
0:00 – 0:15 · 15 MIN
Same ritual every meeting. We get sharper at it; the kids start running it.
01
SAY WATT ROBOTICS · ROV TEAM
WEEK 6 — CONTROL BOX II · 4 / 22
Notes: Standing ritual. Same as every week. The Safety Briefer runs it now if they're ready.

## Slide 5
THE STANDING RITUAL
Every meeting opens with a safety brief.
Why we do this
Real engineering and dive teams brief safety before every job — not because they expect to fail, but because the discipline of asking the same four questions every time is what makes a team safe in the long run. We start the habit now, when the stakes are small, so it's automatic when they aren't.
1
What are we doing today?
2
What could hurt someone?
3
How do we prevent it?
4
Who do we tell if something happens?
TODAY'S BRIEF · MEETING 6
THE WORK
Finish soldering the TriggerFish control box. Build the ROV power wire from battery to board. Terminate the tether at the control box.
THE HAZARDS
Same as 1.5 plus stripped-wire ends (sharp) and 12V DC at the power-wire end once the battery is connected. Battery is OFF during build.
PREVENTION
Battery stays disconnected until pre-power-up review. No exceptions. Same iron, glasses, fume, hand-wash rules as 1.5.
IF SOMETHING HAPPENS
Stop. Disconnect the battery first (if connected). Tell the advisor. Burns get cool water for 15 minutes; cuts get the first-aid kit.
LOOKING AHEAD
1.7 is the capsule build and first pool day. Pool prerequisites — lifeguard, swim checks, photo releases — get confirmed this week, not at the pool deck.
SAY WATT ROBOTICS · ROV TEAM
WEEK 6 — CONTROL BOX II · 5 / 22
Notes: Same standing format as 1.5. The new safety beat tonight is BATTERY STAYS OFF until the pre-power-up review. Hit that line twice — once in the brief, once at the start of section 04.

## Slide 6
SECTION 02
Where the
Board Stands
0:15 – 0:30 · 15 MIN
Inventory what 1.5 closed. Name the open joints. Read the next block from the Guide.
02
SAY WATT ROBOTICS · ROV TEAM
WEEK 6 — CONTROL BOX II · 6 / 22
Notes: Inventory what 1.5 closed. Name the open joints. Read the next block from the Guide.

## Slide 7
TRIGGERFISH REV 4
Where 1.5 left us — and what's left to do.
Coming out of 1.5 the board carries the fuse holder, the two 1000µF / 16V caps, the 3 A practice fuse, and the next block of components per the SeaMATE Guide. Every completed joint should be meter-checked from last week's discipline pass.
Tonight we close the remaining components on the control box itself, build the ROV power wire from battery to board, terminate the tether at the control box, and re-fuse the circuit to the measured full-load amps from the watt meter (the 3 A practice fuse comes out).
We do NOT power the board up tonight. The smoke test waits for 1.7's pre-pool review. The reason is simple: every wiring fault we catch dry is one we don't catch wet.
SAY WATT ROBOTICS · ROV TEAM
WEEK 6 — CONTROL BOX II · 7 / 22
Notes: Walk through this; spend the most time on the headline's verb.

## Slide 8
SECTION 03
Finish the
Control-Box Wiring
0:30 – 1:30 · 60 MIN
Sixty minutes hands on. Same build loop as 1.5: read, stage, solder, inspect, meter.
03
SAY WATT ROBOTICS · ROV TEAM
WEEK 6 — CONTROL BOX II · 8 / 22
Notes: Sixty minutes hands on. Same build loop as 1.5: read, stage, solder, inspect, meter.

## Slide 9
THE BUILD LOOP — UNCHANGED
Read the slide. Stage. Solder. Inspect. Meter. Next.
Same loop as 1.5. We don't get ahead of the Guide.
1
Read the slide as a team
One reader, others listen. No iron picked up until the team agrees on what the slide is asking for.
2
Stage the components
Lay them out next to the board, oriented the way they'll go in. Polarity-sensitive parts marked clearly with a piece of tape or a label.
3
Solder one at a time
Whoever has the iron owns that joint. Others coach, photograph, or cue up the next component.
4
Inspect and meter-check
Shiny, smooth, concave. Continuity to the next pad in the circuit; no shorts to ground or neighboring pads.
5
Move to the next slide
Only when the current step passes inspection AND meter-check. The discipline is what gets us through inspection in April.
SAY WATT ROBOTICS · ROV TEAM
WEEK 6 — CONTROL BOX II · 9 / 22
Notes: Walk through this; spend the most time on the headline's verb.

## Slide 10
BREAK
Ten minutes.
We resume in ten — and, like always, we start on time.
SAY WATT ROBOTICS · ROV TEAM | WEEK 6 — CONTROL BOX II

## Slide 11
SECTION 04
Power Wire +
Tether
1:40 – 2:25 · 45 MIN
From battery to board. From board to tether. Strain relief at every termination.
04
SAY WATT ROBOTICS · ROV TEAM
WEEK 6 — CONTROL BOX II · 11 / 22
Notes: Power wire AND tether termination. Polarity twice. Strain relief on every termination.

## Slide 12
THE POWER WIRE
Battery to board. Three things matter.
GAUGE
Heavy enough to carry the measured full-load amps without voltage drop. The team's spec for the TriggerFish: 14 AWG silicone-jacketed, two conductors red/black, ring terminals at the battery end.
POLARITY
Red to positive, black to negative — at BOTH ends. Marked clearly. Reversed polarity at the board feeds the wrong rail and ends the night. Two people verify before commit.
STRAIN RELIEF
Heatshrink + cable tie at the board end. The wire must not be the load-bearing member if someone trips over it. Tape and zip ties as primary strain relief fail safety inspection in April.
SAY WATT ROBOTICS · ROV TEAM
WEEK 6 — CONTROL BOX II · 12 / 22
Notes: Walk through this; spend the most time on the headline's verb.

## Slide 13
THE TETHER
Pre-terminated. Strain relief at both ends.
CONTROL BOX END
Tether conductors terminate at the control box per the SeaMATE Guide. Each conductor is meter-checked end-to-end before the heatshrink goes on the splice.
ROV END
The other end gets terminated to the thrusters and cameras in 1.8. Tonight we land the control-box end and verify continuity through every conductor.
SAY WATT ROBOTICS · ROV TEAM
WEEK 6 — CONTROL BOX II · 13 / 22
Notes: Walk through this; spend the most time on the headline's verb.

## Slide 14
SECTION 05
The Fuse
Lives by Measurement
2:25 – 2:40 · 15 MIN
Watt meter reads the full-load amps. The fuse sizes one step above. That number lives in the engineering notebook.
05
SAY WATT ROBOTICS · ROV TEAM
WEEK 6 — CONTROL BOX II · 14 / 22
Notes: Fuse selection from measurement. This is the section that wins safety inspection in April.

## Slide 15
FUSE SELECTION
Measure. Round up to the next blade size. Document.
MATE safety inspection asks for the FLA math. The team that has it cited from a measurement passes clean.
1
Measure full-load amps with the watt meter
Battery connected ONLY to the watt meter (not the board). All thrusters and electronics at simulated full-load if possible; if not, the highest measured draw from 1.5 / 1.6 stages plus a safety margin.
2
Round up to the next standard blade-fuse size
If measured FLA is 4.2 A, fuse at 5 A. If 7.1 A, fuse at 10 A. Standard blade sizes — 3 / 5 / 7.5 / 10 / 15 / 20 A. The 3 A practice fuse comes out tonight.
3
Document in the engineering notebook
Measured FLA. Fuse size selected. Citation: ELEC-NRD-003 (the MATE rule that requires the fuse to be sized from measured draw, not guessed).
4
Install and verify the new fuse seats cleanly
New fuse in the holder. Multimeter continuity through the holder. Photograph the holder + the engineering-notebook entry side by side.
SAY WATT ROBOTICS · ROV TEAM
WEEK 6 — CONTROL BOX II · 15 / 22
Notes: Walk through this; spend the most time on the headline's verb.

## Slide 16
SECTION 06
Pre-Power-Up
Meter-Check
2:40 – 3:00 · 20 MIN
Every pad. Three reads. Sign the board off before we leave.
06
SAY WATT ROBOTICS · ROV TEAM
WEEK 6 — CONTROL BOX II · 16 / 22
Notes: Pre-power-up meter-check. Every pad. Three reads. Sign the board off.

## Slide 17
THE THREE READS — EVERY PAD
If we miss a short tonight, we find it the loud way next week.
1
Continuity from every pad to its intended next pad
Walk the schematic with the multimeter. Every connection on the slide gets a beep at the bench. Silence means re-route or re-flow.
2
No shorts to ground or to neighboring pads
Probe every pad against ground and against immediate neighbors. Beep here means a solder bridge — fix it tonight.
3
Polarity confirmed at the power-wire termination
Red to positive rail. Black to negative rail. Eyes on the board, eyes on the Guide, eyes on the wire. Three references; one orientation.
4
Sign the board off in the engineering notebook
Whoever did the final meter-check signs the page. Date, time, results. That signature is the answer when a judge asks 'who verified this?' in April.
SAY WATT ROBOTICS · ROV TEAM
WEEK 6 — CONTROL BOX II · 17 / 22
Notes: Walk through this; spend the most time on the headline's verb.

## Slide 18
SECTION 07
Wrap-Up &
Homework
3:00 – 3:00 · 0 MIN
Capture what we decided. Close the loop. Hand off the next move.
07
SAY WATT ROBOTICS · ROV TEAM
WEEK 6 — CONTROL BOX II · 18 / 22
Notes: Wrap-up. Pool prerequisites confirmed before we leave the room.

## Slide 19
WRAP-UP & HOMEWORK
Before we meet again.
EVERY STUDENT
1
Pool prerequisites for 1.7 — confirm with your parents that your photo-release form is signed and your swim-comfort form is on file. We do not get in the water without both.
2
Re-read the SeaMATE Guide sections on capsule construction. The kit doesn't come with capsules — we build them in 1.7.
3
Bring closed-toe shoes AND a towel + change of clothes next week. The capsule drop is on a pool deck.
THE PARALLEL TRACK · LEADS & ADVISORS
Advisors: confirm lifeguard coverage, host pool rules in writing, photo releases returned for every kid expected in frame. These are the gating items for 1.7 — without any one of them, the pool day slips a week.
NEXT MEETING · WEEK 7
Capsule Build & First Splash
Build the watertight capsules — PVC, end caps, O-rings, marine epoxy. Pool deck. Every kid in the water. Capsule drop #1: assemble dry, drop wet, retrieve, check the towel inside, log the result.
SAY WATT ROBOTICS · ROV TEAM
WEEK 6 — CONTROL BOX II · 19 / 22
Notes: Read the three student items. Confirm each has an owner. Hand off to the Notetaker for the action-items slide. Then the tool-checkout slide; Tool Steward leads.

## Slide 20
ACTION ITEMS
What we decided. Who owns it. When it's due.
The Notetaker fills these in during the meeting and reads them back before we leave.
ITEM
OWNER
DUE
SAY WATT ROBOTICS · ROV TEAM
WEEK 6 — CONTROL BOX II · 20 / 22
Notes: Notetaker fills these in live as decisions are made. Read back before the closer.

## Slide 21
BEFORE WE LEAVE
Tools accounted for. Shop reset.
We do this together, every meeting. No exceptions — the Tool Steward leads.
Soldering irons unplugged, cool, and put away.
Control box secured in its tray; power wire and tether coiled neatly beside it.
Battery STILL DISCONNECTED — confirmed by two people before leaving the room.
Multimeter and watt meter back in their cases.
Workshop swept; benches wiped; sharps disposed.
Today's photos uploaded to the team folder.
Notetaker's meeting notes filed with the CFO for the engineering notebook.
SAY WATT ROBOTICS · ROV TEAM
WEEK 6 — CONTROL BOX II · 21 / 22
Notes: Tool Steward leads. Every kid stays until the workshop is reset.

## Slide 22
THE BOARD IS DONE. THE BOX IS READY.
Next week, the capsules — and the pool.
Smoke test happens during 1.7's pre-pool review. If the meter-check holds, we power up and we drop the first capsule the same day.
SAY WATT ROBOTICS · ROV TEAM | NEXT MEETING — WEEK 7, CAPSULE BUILD & FIRST SPLASH
Notes: Dark slide. Read the statement, pause, read the summary. The kids should leave knowing the pool is next week. ~30 seconds.