## Slide 1
PHASE 1 — FOUNDATION
The Kit Comes Out
Inventory the Triggerfish, then make its first connections.
Say Watt Robotics · ROV Team | 2026–2027 MATE ROV Season
CLASS 1.3 · ONE SESSION · MADISON, ALABAMA
Notes: Open with energy — this is the week the team has waited for: today everyone solders. 30 seconds here. Set the tone — it is our longest meeting, by design, and the work is worth the time.

## Slide 2
THE MEETING
Three hours, the kit comes alive.
0:00
Welcome & Safety Brief
15 min
0:15
Unbox & Inventory the Kit
35 min
0:50
Read the Build Sequence
20 min
1:10
First Real Connections
50 min
2:00
Break
10 min
2:10
Open the Three Records
25 min
2:35
Design the Capsule
15 min
2:50
Wrap-up & homework
10 min
We run on time. Every block has a clock, and we hold to it — that habit is part of the engineering.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.3 — KIT UNBOXING & FIRST ELECTRONICS · 2 / 18
Notes: Walk the eight blocks quickly, then land one point: this is our longest day, about three and a half hours. If a block runs long, we protect the hands-on practice and trim elsewhere — we never cut the time on the iron. Note the break at 1:55.

## Slide 3
TODAY'S ROLES
Four jobs. Four students. Different every week.
Every meeting we assign these four — by season's end, every student has done every job.
NOTETAKER / SCRIBE
TODAY: __________________________________
Captures every decision, action item, and blocker. Files notes with the CFO for the engineering notebook.
SAFETY BRIEFER
TODAY: __________________________________
Delivers the standing four-question safety brief at the start of the meeting.
PHOTOGRAPHER
TODAY: __________________________________
Captures photos and short videos throughout — feeds the engineering notebook and the marketing display.
TIMEKEEPER
TODAY: __________________________________
Holds the meeting to the agenda's clock. Calls the time at each block change.
SAY WATT ROBOTICS · ROV TEAM
WEEK 3 — KIT UNBOXING · 3 / 18

## Slide 4
01
SECTION 01
Welcome &
Safety Brief
0:00 – 0:15 · 15 MIN
Every meeting we ever hold will begin in exactly this place.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.3 — KIT UNBOXING & FIRST ELECTRONICS · 4 / 18
Notes: Same opening as always. Let the CEO run the safety brief if roles are set — 60 to 90 seconds. The ritual matters more today than ever: there are hot irons in the room.

## Slide 5
THE STANDING RITUAL
Every meeting opens with a safety brief.
Why we do this
Real engineering and dive teams brief safety before every job — not because something went wrong, but so it never does. We adopt the same habit on day one. Sixty seconds, every meeting, no exceptions.
Each brief answers the same four questions, so the team always knows what to expect.
1
What are we doing today?
2
What could hurt someone?
3
How do we prevent it?
4
Who do we tell if something happens?
TODAY'S BRIEF · CLASS 1.3
THE WORK
Unboxing the kit, the first kit electronics, and opening the team's records.
THE HAZARDS
Hot irons again; small parts and sharp tools; lead in solder.
PREVENTION
Irons in stands, fume fan on, glasses down. Count and bag small parts so none walk off. Wash hands after solder.
IF SOMETHING HAPPENS
Cool a burn under running water, tell the advisor, and log it. A missing part gets flagged the same day.
LOOKING AHEAD
Class 1.4 — the multimeter and learning to read a circuit.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.3 — KIT UNBOXING & FIRST ELECTRONICS · 5 / 18
Notes: The most important safety brief of the season so far. Slow down on hazards and prevention. Irons live in their stands, never on the bench. Confirm the fume fan is on and everyone has glasses before any iron is powered. Read ‘every burn gets reported’ out loud.

## Slide 6
02
SECTION 02
The Kit
Comes Out
0:15 – 0:50 · 35 MIN
The Triggerfish leaves the box, gets counted against the manual, and the first real electronics go in.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.3 — KIT UNBOXING & FIRST ELECTRONICS · 6 / 18
Notes: Shift gears — the kit comes out now, 55 minutes for unboxing and the first real electronics. The Mechanical Lead leads.

## Slide 7
THE KIT COMES OUT
Unbox it. Count every part.
The SeaMATE Triggerfish is our trainer ROV — the kit every kid learns on before we build the competition vehicle. The moment it opens, the Mechanical Lead runs inventory against the manual’s parts list.
One rule: nothing gets built until every part is counted and checked off. A missing part found today is an email; found mid-build, it is a lost week.
QTY
PART
NOTE
✓
3
Thruster motors
Handle by the body, not the leads
☐
1 set
Frame & hardware
Count every screw
☐
DON’T FORGET
It ships without a power source.
The Triggerfish kit does not include a battery. Our 12 V SLA battery, charger, and Powerpole leads are a separate order — and they must be in hand before the wiring lesson.
OWNER Mechanical Lead
STATUS Battery on order · due before wiring
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.3 — KIT UNBOXING & FIRST ELECTRONICS · 7 / 18
Notes: Hand the manual to the Mechanical Lead and let them run inventory — do not do it for them. The one rule: count everything before building. Flag the side card out loud — the kit has no battery, and ours must arrive before Week 3. This is a live open item.

## Slide 8
03
SECTION 03
First
Electronics
0:50 – 1:10 · 70 MIN
Irons hot again — the joints we practiced become real connections on the robot.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.3 — KIT UNBOXING & FIRST ELECTRONICS · 8 / 18
Notes: Short divider, 15 minutes. Set up the why before the how: nobody picks up an iron until they understand what a good joint is and why it matters.

## Slide 9
FIRST ELECTRONICS
Read the manual. Then wire stage one.
1
Read the build order
Walk the manual’s sequence start to finish before touching a part, so everyone knows the whole path.
2
Lay out stage one
Group the parts for the first stage and match each one to the diagram. Ask questions now, not mid-solder.
3
Make the first kit joints
The irons are already hot. The joints we practiced become real connections on the robot.
4
Photograph and log it
Shoot the stage, write what we did and any decision we made. The notebook fills as the robot grows.
Two things to remember. We stop wherever the clock runs out. A clean stopping point always beats a rushed connection.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.3 — KIT UNBOXING & FIRST ELECTRONICS · 9 / 18
Notes: Read the manual’s build order together before touching parts. Then start stage one with irons already hot — the practice joints become real connections now. Stop at a clean point when the clock runs out; never rush a connection.

## Slide 10
04
SECTION 04
The Records
Begin Today
2:10 – 2:35 · 25 MIN
Five records that win in April start quietly today — repo, wiki, notebook, photos, outreach.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.3 — KIT UNBOXING & FIRST ELECTRONICS · 10 / 18
Notes: Quick divider, 15 minutes for the records. They feel like overhead now but they win points in April. The Software Lead drives the GitHub setup.

## Slide 11
THE RECORDS
Five records open today and never close.
The build is only half the season. The documentation, the code, and the outreach are scored too — and like a joint, they are honest only if made as we go. Five records start now.
1
GitHub org
The Software Lead creates the team’s GitHub organization on student accounts. All code lives here.
2
Project wiki
A shared wiki for how-tos, wiring notes, and decisions the whole team can read and edit.
3
Project notebook
Every decision, with its reason. Written as we go — a notebook from memory is fiction.
4
Photo log
Photograph the work every meeting. These pictures become the marketing display and the report.
5
Outreach log
Log everyone we teach or reach. Outreach is scored and cannot be faked in April.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.3 — KIT UNBOXING & FIRST ELECTRONICS · 11 / 18
Notes: Move fast across the five — open each record today, do not perfect it. Land the notebook point: written as we go is honest; written from memory is fiction. Assign owners out loud.

## Slide 12
05
SECTION 05
The Waterproof
Capsule
2:35 – 2:50 · 15 MIN
A five-dollar dress rehearsal for the float that must survive 2.5 meters.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.3 — KIT UNBOXING & FIRST ELECTRONICS · 12 / 18
Notes: Short divider. Frame the capsule as a five-dollar rehearsal for the Phase 2 float. 10 minutes — this is design on paper today, not building.

## Slide 13
THE WATERPROOF CAPSULE
Keep a paper towel dry. Underwater.
Each kid designs a small waterproof capsule — a sealed PVC body with a single cable passing through the wall. The test could not be simpler: a paper towel sealed inside has to come out bone dry after a dunk.
It is the same problem the Phase 2 float must solve at 2.5 meters, where a leak ends the mission. Here it costs five dollars and a do-over. Sketch your design today; we cut and seal next week.
One body, one cable penetration, zero leaks. Draw your plan before you leave today.
THE BRIEF
Seal the body. Seal the cable. Prove it stays dry.
Due today: your sketch
Every student designs one. We cut and seal them for real in a later lesson.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.3 — KIT UNBOXING & FIRST ELECTRONICS · 13 / 18
Notes: Keep it playful: keep a paper towel dry, underwater. Each kid sketches one body, one cable, and a seal plan. Do not over-engineer it for them — let them propose. Sketches are due before they leave; the first dunk test is Week 3.

## Slide 14
06
SECTION 06
Wrap-Up &
Homework
2:50 – 3:00 · 10 MIN
Close the loop: what each student carries out, and what the team carries forward into the water.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.3 — KIT UNBOXING & FIRST ELECTRONICS · 14 / 18
Notes: Final divider — 10 minutes to close the loop. Make sure every kid leaves knowing their homework and the team knows the parallel-track items.

## Slide 15
WRAP-UP & HOMEWORK
Before we meet again.
EVERY STUDENT
1
Finish your capsule sketch — one body, one cable, a plan to stay dry.
2
Software Lead: confirm everyone can log in to the GitHub org.
3
Watch the Class 1.4 pre-watch (Multimeter Basics) when assigned.
THE PARALLEL TRACK · LEADS & ADVISORS
Battery, charger, and leads in hand before the electronics workshop. SeaMATE Simple Circuits Lab Kits on order. Pool prerequisites moving — lifeguard, swim checks, host rules in writing.
NEXT LESSON · CLASS 1.4
Electronics
Workshop
The multimeter, switches, simple circuits, and the Electrical Symbols handout — learning to read a circuit.
SAY WATT ROBOTICS · ROV TEAM
CLASS 1.3 — KIT UNBOXING & FIRST ELECTRONICS · 15 / 18
Notes: Three things for students, no more — keep it light. Read the parallel-track card to the parents: battery before Week 3, pool prerequisites, and the DISL call. These gate the water. Preview Week 3 — electronics finished and the first splash.

## Slide 16
ACTION ITEMS
What we decided. Who owns it. When it's due.
The Notetaker fills these in during the meeting and reads them back before we leave.
ITEM
OWNER
DUE
SAY WATT ROBOTICS · ROV TEAM
WEEK 3 — KIT UNBOXING · 16 / 18

## Slide 17
BEFORE WE LEAVE
Tools accounted for. Shop reset.
We do this together, every meeting. No exceptions — the Tool Steward leads.
Soldering irons unplugged, cool, and put away.
All hand tools and test equipment back in their bins.
Batteries off charge; charger stations powered down.
Workshop swept; benches wiped; trash out.
Today's photos uploaded to the team folder.
Notetaker's meeting notes filed with the CFO for the engineering notebook.
SAY WATT ROBOTICS · ROV TEAM
WEEK 3 — KIT UNBOXING · 17 / 18

## Slide 18
THE KIT IS ALIVE
It’s a robot now.
The Triggerfish is inventoried, its first connections are made, the records are open, and every capsule is designed.
Next, we learn to read it.
SAY WATT ROBOTICS · ROV TEAM | NEXT LESSON — CLASS 1.4, ELECTRONICS WORKSHOP
Notes: Close with pride — everyone soldered today, the kit is open, the first joints are on the robot. Land the final line: next week, it gets wet. Send them out energized for the first splash.